## Slide 1
Application of a Master-Worker Parallelism on Materials Modelling
PAX-HPC Meeting, Lancaster, 22th April 2024
Woongkyu Jee, University College London

## Slide 2
W. Jee, PAX-HPC Meeting, Lancaster, 22th April 2024
On today’s talk
Introduction Modelling stochastic processes in materials science (e.g., ion-batteries/conductors, solid-oxide fuel cell, etcs.)
Master-Worker Parallelism and application Implementation of the master-worker parallelism Profiling results on ARCHER 2 Issues
Outlook Future plan (upcoming tasks)

## Slide 3
W. Jee, PAX-HPC Meeting, Lancaster, 22th April 2024
Fig 1 Schematic diagram of discharging reaction in a Li-ion battery
Introduction
Modelling stochastic processes in materials science
Mobile devices
Battery packs in EV
Fig 2 Ceria as electrolyte materials in hydrogen fuel cells doi.org/10.1016/j.electacta.2021.139067
Fig 2 Market expectation of various cathode materials

## Slide 4
Introduction
stochastic processes in materials science
W. Jee, PAX-HPC Meeting, Lancaster, 22th April 2024
W. Jee et al, 2024
Fig 1 Li intercalation energy distribution and the global minimum structure of Ramsdellite LixMnO2.
X. Zhang et al, 2024
Fig 2 Understanding order and disorder in reduced Ceria SOFC by large-scale Monte-Carlo simulations
Other Projects
Neutral Atom Quantum Annealing for the Configurational Analysis of Solid Solutions, B. Camino.
Study of Magnesium Intercalation Mechanism in Spinel-MnO2, J. A. Nasir.

## Slide 5
Introduction
stochastic processes in materials science
1. Monte-Calro appraoch
For instance, sampling Li intercalation sites in LixMnO2
W. Jee, PAX-HPC Meeting, Lancaster, 22th April 2024
Fig 1 (a) Possible Li intercalation sites (green spheres) and (b) the energy density of states with selected different number of samples.
2. Apply statistical mechanics
Canonical
Grand canonical
3. Calculate desired properties
Fig 2 Calculated and experimental voltage profile of LixMnO2.
Na2/3FePO4 crystal structure
Fig 3 Calculated and experimental voltage profile of NaxFePO4.

## Slide 6
1. Monte-Calro appraoch
For instance, sampling Li intercalation sites in LixMnO2
W. Jee, PAX-HPC Meeting, Lancaster, 22th April 2024
Fig 1 (a) Possible Li intercalation sites (green spheres) and (b) the energy density of states with selected different number of samples.
Master-Worker Parallelism
Introducing Master-worker parallelism
Stochastic energy sampling
Introducing Master-Worker Parallelism
Calculating energies of each samples are independent
Master CPU
Materials Application
Task Manager
Send-Recv
Packaging/Collecting
Task Queue
MPI enabled App
worker 1
MPI enabled App
worker 2
MPI enabled App
worker n
HPC node 1
…
MPI enabled App
worker 1
MPI enabled App
worker 2
MPI enabled App
worker n
HPC node 2
…
MPI enabled App
worker 1
MPI enabled App
worker 2
MPI enabled App
worker n
HPC node N
…
Task 1
Task 2
…
Task N
Task Queue
Task 3
Task 4

## Slide 7
W. Jee, PAX-HPC Meeting, Lancaster, 22th April 2024
Master-Worker Parallelism
Implementation
/* main program */
void main() {
ConfigureCommunicator();
…
if( rank == master )
Master();
else
Worker();
…
return;

## Slide 8
W. Jee, PAX-HPC Meeting, Lancaster, 22th April 2024
Master-Worker Parallelism
Implementation: Configure Communicator
ConfigureCommunicator();
/* main program */
void main() {
ConfigureCommunicator();
…
if( rank == master )
Master();
else
Worker();
…
return;
Splitting Resource
BaseComm (master)
SubComm (worker or workgroup)
Notes: Keeping ‘subcomm_tag’ will be useful to access desired ‘subcomm (or worker)’ later!

## Slide 9
W. Jee, PAX-HPC Meeting, Lancaster, 22th April 2024
Master-Worker Parallelism
Implementation: Master()
Master();
/* main program */
void main() {
ConfigureCommunicator();
…
if( rank == master )
Master();
else
Worker();
…
return;

## Slide 10
W. Jee, PAX-HPC Meeting, Lancaster, 22th April 2024
Master();
/* main program */
void main() {
ConfigureCommunicator();
…
if( rank == master )
Master();
else
Worker();
…
return;
Init_tasks();
Filling-up the TaskQueue. Each task may require desired input-files or information
Read-in input files from disk
For runtime generation in worker-level, setting-up desired instructions.
Master-Worker Parallelism
Implementation: Master()

## Slide 11
W. Jee, PAX-HPC Meeting, Lancaster, 22th April 2024
Master();
/* main program */
void main() {
ConfigureCommunicator();
…
if( rank == master )
Master();
else
Worker();
…
return;
Initial Task Messaging
GetNextTask() return a task from TaskQueue
Master-Worker Parallelism
Implementation: Master()

## Slide 12
W. Jee, PAX-HPC Meeting, Lancaster, 22th April 2024
Master();
/* main program */
void main() {
ConfigureCommunicator();
…
if( rank == master )
Master();
else
Worker();
…
return;
Recv-Send
Recv Task (which could be a derived datatype, including desired task results, e.g., struct, class, module …)
Send Task, sending next task in the TaskQueue.
Master-Worker Parallelism
Implementation: Master()
Notes: Send Task, this message could be sent to where the right previous Recv message came from. (RECV->SEND-BACK)
If TasksQueue is empty. For instance, returned NULL or False, call break the for loop and send ’kill message’ to workers. (kill message is for asking them to return).

## Slide 13
W. Jee, PAX-HPC Meeting, Lancaster, 22th April 2024
Worker();
/* main program */
void main() {
ConfigureCommunicator();
…
if( rank == master )
Master();
else
Worker();
…
return;
Master-Worker Parallelism
Implementation: Worker()
Notes: Worker also include infinite loop, waiting for task message from Master.

## Slide 14
W. Jee, PAX-HPC Meeting, Lancaster, 22th April 2024
Worker();
/* main program */
void main() {
ConfigureCommunicator();
…
if( rank == master )
Master();
else
Worker();
…
return;
Recv Task
If received task message is valid, do computation. Computation includes launching materials application. materials application can be launched through (1) system call or (2) called as a function.
Master-Worker Parallelism
Implementation: Worker()
Notes: Send Task, this message could be sent to where the right previous Recv message came from. (RECV->SEND-BACK)
If TasksQueue is empty. For instance, returned NULL or False, call break the for loop and send ’kill message’ to workers. (kill message is for asking them to return).

## Slide 15
W. Jee, PAX-HPC Meeting, Lancaster, 22th April 2024
Worker();
/* main program */
void main() {
ConfigureCommunicator();
…
if( rank == master )
Master();
else
Worker();
…
return;
Send Task (result)
Send task result back to master (result may include desired information taken from the materials application)
Master-Worker Parallelism
Implementation: Worker()
Notes: Send Task, this message could be sent to where the right previous Recv message came from. (RECV->SEND-BACK)
If TasksQueue is empty. For instance, returned NULL or False, call break the for loop and send ’kill message’ to workers. (kill message is for asking them to return).

## Slide 16
Master-Worker Parallelism
Profiling on ARCHER 2
Master
Worker
Closer look of a Worker communicating with Master
Master (time)
Worker (time)
Master
Recv / Send
…
…
app_elapsed_t
Master
Recv / Send
Master
Recvt – Sendt
Worker
Sendt – Recvt
application-level measured ~ pure computation time consumed by the application
overhead from before (unpacking task and preparing app-launching) and after (packing result) launching application
overhead from MPI (Send/Recv) + Master-Worker architecture (delay in Master looping workers)
W. Jee, PAX-HPC Meeting, Lancaster, 22th April 2024
Notes: Red (application level elapt) : ‘app_elap_t’
Green: ‘app_launch_overhead’
Blue: ’mpi_overhead’

## Slide 17
Master-Worker Parallelism
Profiling on ARCHER 2
W. Jee, PAX-HPC Meeting, Lancaster, 22th April 2024
Na2/3FePO4 crystal structure
~ 400 atoms
Na2/3FePO4 100,000 samples (energy model: IP - GULP)
ARCHER 2 : 64 nodes 16 cores per worker (512 workers)
Using prepared TaskQueue from disk (i.e., no preparation overhead)
Overheads (blue/green) are negligible compared to application runtime (red)
Notes: Na2/3FePO4 - 400 atoms system

## Slide 18
Master-Worker Parallelism
Profiling on ARCHER 2 - Overview
W. Jee, PAX-HPC Meeting, Lancaster, 22th April 2024
14.26 s
Na2/3FePO4 100,000 samples (energy model: IP - GULP)
ARCHER 2 : 64 nodes 16 cores per worker (512 workers)
Using prepared TaskQueue from disk (i.e., no preparation overhead)
14.26 / 512 = 0.02785 seconds (MPI_Send) per workgroup
Notes: Na2/3FePO4 - 400 atoms system
14.26 / 512 = 0.02785 seconds (MPI_Send per workgroup)

## Slide 19
Master-Worker Parallelism
Profiling on ARCHER 2 - Overview
W. Jee, PAX-HPC Meeting, Lancaster, 22th April 2024
Na2/3FePO4 100,000 samples (energy model: IP - GULP)
ARCHER 2 : 64 nodes 16 cores per worker (512 workers)
Using prepared TaskQueue from disk (i.e., no preparation overhead)
main program return
Ave. time
160.78 s
160.78 s : such late delay varies depending on samples.
Notes: Na2/3FePO4 - 400 atoms system

## Slide 20
Master-Worker Parallelism
Profiling on ARCHER 2 – Initial delay
W. Jee, PAX-HPC Meeting, Lancaster, 22th April 2024
64 nodes 16 cores per worker (512 workers)
128 nodes 16 cores per worker (1024 workers)
256 nodes 16 cores per worker (2048 workers)
14.26 s
26.33 s
51.29 s
0.02785 seconds (MPI_Send) per workgroup
0.02572 seconds (MPI_Send) per workgroup
0.02504 seconds (MPI_Send) per workgroup
Initial delay scales up linearly
Necessary to introduce multiple masters to reduce this delay?
Notes: Na2/3FePO4 - 400 atoms system

## Slide 21
Master-Worker Parallelism
Profiling on ARCHER 2 – late delay
W. Jee, PAX-HPC Meeting, Lancaster, 22th April 2024
64 nodes 16 cores per worker (512 workers)
128 nodes 16 cores per worker (1024 workers)
256 nodes 16 cores per worker (2048 workers)
4.18 % out of 3843.74 s (total elapsed time)
8.79 % out of 2044.69 s (total elapsed time)
15.32 % out of 1122.42 s (total elapsed time)
These late delays can be caused by …
Undesired behaviour of application (e.g., energy relaxation got stuck, usually caused by unphysical initial atomic configuration, etcs)
160.78 s
171.71 s
171.93 s
Ave. time
main program return
Possible solutions?
Limit the number of maximum energy relaxation cycles
Apply pre-screener to filter undesired initial configuration
Fundamentally? Limit the runtime in application level (pass the runtime as an input parameter).
Notes: Trial run (single node – get optimal size) – main run (many nodes)
More extreme case – 256 nodes with 4 cores per worker
Typically, increasing cores (after certain number) linear scaling (ideal speed up) breaks. And therefore allocating small number of cpus per worker will be ideal.
However, when this type of late delay occurs, since small number of cores result in much more delay. This is because, for a given number of relaxation cycles for the sample (if system is large) it takes more time to run over, while the rest of worker already finished their tasks and waiting!!!

## Slide 22
Master-worker parallelism is implemented in KLMC (Knowledge-Led Master Code)
KLMC is linked to GULP & FHIaims library Fortran stop is destructive (crashing entire program, instead of returning back to main) Subroutines in GULP – stopnow() / FHIaims – aims_stop() This occurs, when application finds something that doesn’t look right For instance, * unphysical atomic configuration (GULP and FHIaims) * undesired input tolerance used – lowering accuracy – call stop SCF convergence (FHIaims)
Master-Worker Parallelism
Possible pitfalls of using libridised materials application
W. Jee, PAX-HPC Meeting, Lancaster, 22th April 2024
Solution?
Notes: unphysical atomic configuration (GULP and FHIaims) This could be tackled by applying pre-screening filter in KLMC level.

## Slide 23
Master-worker parallelism is implemented in KLMC (Knowledge-Led Master Code)
KLMC is designed to support various types of stochastic sampling: 1. Solid Solutions 2. Basin-Hopping or Random Quenching 3. Genetic algorithm for nanoclusters 4. Nanoclusters on surfaces 5. Simulated annealing – Metropolis Monte-Carlo
As materials simulation applications, supporting: GULP (2023) and FHI-aims (2023)
Outlook
Upcoming Tasks
W. Jee, PAX-HPC Meeting, Lancaster, 22th April 2024

## Slide 24
Thank you very much for your attention
W. Jee, PAX-HPC Meeting, Lancaster, 22th April 2024